## Slide 1: The Arduino Uno
Prototyping board
  8-bit Atmega 328P microcontroller
  Digital I/O pins
  Type-B USB port controlled by Atmega 16U2 IC
Can program the microcontroller
  Programs written to chip over serial USB connection
  Language based on C/C++
  Python wrapper available
Notes: Talk about FIRMWARE issue when 16U2 is mentioned
More familiar with Python (NEXT SLIDE to explain why chose C++)

## Slide 2: Programming and Development
Used C++
  Compiled not interpreted
  Libraries for IR detector available
Revision control with GitHub
Controlled a number of devices
  Stepper motor
  LED/display
  This powerpoint

## Slide 3: Operational Details
Arduino 1
  Receives signal
  If AV, wait for numbers
  Display each number as it is pressed
  After third number, move motor to that position
Arduino 2
  Receives signal
  If arrow key, write to serial
  Listener program reads serial
  Sends key-press signal to OS to change slide

## Slide 4: Demonstration
Set a position
  Numbers pressed show on display
  Motor moves to that position
Angles are relative to a reference position, not current position
Pressing AV before 3rd digit allows re-entering
Display set efficiently using PORTD register
Notes: Demonstrate functions as shown on slide, easy peasy.